## Slide 1: DIGITAL LOGIC DESIGN (111776)
Dr. Owais Hussain

## Slide 2: Agenda
Multiplexers
2-1 MUX
4-1 MUX
8-1 MUX
N-1 MUX
Constructing N-1 MUX using Multiple MUXs
MUX as Universal gate
Demultiplexers
Difference b/w MUX & DEMUX

## Slide 3: Sample 2
Multiplexers
A Multiplexer (shortly MUX) is a combinational circuit, which allows selecting from multiple input signals into a single output.
The input of a Multiplexer is up to signals and a set of select lines (also called switches).
The select lines determine which input signal will be passed to the output
MUXs can be combined to create larger circuits that can handle more input lines and create complex logical functions.

## Slide 4: Sample 2
Multiplexers
The range of input signals from contain the input data.
The output will be one of the inputs. The select lines choose which of the input will become the output.

## Slide 5: Sample 2
2-1 MUX
The input signals are , i.e., and since therefore there will be single switch .
We do not know what the input values will be in the input lines. The output Q will be or
Truth Table
Logic Expression
Logic Circuit
0 | 
1 | 
0 | 
1 | 

## Slide 6: Sample 2
4-1 MUX
The input signals are , i.e., and since therefore there will be two switches . (You can choose any letters you want for Input and Output for to your convenience).
The output Q will be one of the input lines
Truth Table
Logic Expression
Logic Circuit
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 7: Sample 2
8-1 MUX
The input signals are , i.e., to and since therefore there will be two switches
Truth Table
Can you find out the logic expression ?
Logic diagram
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 

## Slide 8: Sample 2
8-1 MUX

## Slide 9: Sample 2
N-1 MUX
The input signals are , i.e., to
There will be switches to
Truth Table
Block diagram
 |  |  | … |  | 
0 | 0 | 0 | … | 0 | 
1 | 0 | 0 | … | 0 | 
0 | 1 | 0 | … | 0 | 
1 | 1 | 0 | … | 0 | 
0 | 0 | 1 | … | 0 | 
1 | 0 | 1 | … | 0 | 
… | … | … | … | … | 
… | … | … | … | … | 
 |  |  | … |  | 
0 | 0 | 0 | … | 0 | 
1 | 0 | 0 | … | 0 | 
0 | 1 | 0 | … | 0 | 
1 | 1 | 0 | … | 0 | 
0 | 0 | 1 | … | 0 | 
1 | 0 | 1 | … | 0 | 
… | … | … | … | … | 
… | … | … | … | … | 

## Slide 10: Sample 2
Constructing N-1 MUX using Multiple MUXs
4-1 MUX using 2-1 MUXs
We use 3 MUXs of 2-1 to construct a 4-1 MUX.
First MUX will collect input from ; Second MUX will collect input from
Switch is LSB, therefore it will go to both the MUXs
Finally, the output from both MUXs will be combined into 3rd MUX withas its selection switch.
Notes: Exercise: Suppose the input is the Binary for for number 9. Simulate the circuit using
Exercise: Suppose the input 𝐼 is the Binary for for number 9. Simulate the circuit using 𝑆_0=1;𝑆_1=1

## Slide 11: Sample 2
Constructing N-1 MUX using Multiple MUXs
16-1 MUX using 4-1 MUXs
We use 5 MUXs of 4-1 to construct a 16-1 MUX.
First MUX will collect input from ; Second MUX will collect input from and likewise
Switch are LSBs, therefore they will go to first 4 MUXs
Finally, the output from all MUXs will be combined into 5th MUX with as selection switches.
Notes: Exercise: Suppose the input is the Binary for for number 9. Simulate the circuit using
Exercise: Suppose the input 𝐼 is the Binary for for number 9. Simulate the circuit using 𝑆_0=1;𝑆_1=1

## Slide 12: Sample 2
MUX as Universal Gate
AND gate
OR gate
Can you make NOT gate?
Notes: Yes, NOT gate can easily be made. If we supply as input to switch; and then will be .
Yes, NOT gate can easily be made. If we supply 𝑥 as input to switch; 𝐼_0=1 and 𝐼_1=0 then 𝑦 will be 𝑥′.

## Slide 13: Sample 2
Demultiplexers
Demultiplexers or DEMUXs do exactly the opposite of MUXs.
There is single input and number of switches to decide which output channel to pass the input to.
Notes: Yes, NOT gate can easily be made. If we supply 𝑥 as input to switch; 𝐼_0=1 and 𝐼_1=0 then 𝑦 will be 𝑥′.

## Slide 14: Sample 2
Differences between MUX and DEMUX
MUX converts various input signals into single output.
Known as Data Selector.
It has input and selection lines.
In time division Multiplexing, it is used on transmitter end.
DEMUX converts single input signal into various outputs.
Known as Data Distributor.
It has 1 input and selection lines.
In time division Multiplexing, it is used on receiver end.
Notes: Yes, NOT gate can easily be made. If we supply 𝑥 as input to switch; 𝐼_0=1 and 𝐼_1=0 then 𝑦 will be 𝑥′.

## Slide 15: Sample 2
1-4 DEMUX
The input is with 2 switch lines; therefore, there will be output lines.
The logic circuit can easily be derived from this truth table.
0 | 0 | 0 or 1 |  | 0 | 0 | 0
0 | 1 | 0 or 1 | 0 |  | 0 | 0
1 | 0 | 0 or 1 | 0 | 0 |  | 0
1 | 1 | 0 or 1 | 0 | 0 | 0 | 
0 | 0 | 0 or 1 |  | 0 | 0 | 0
0 | 1 | 0 or 1 | 0 |  | 0 | 0
1 | 0 | 0 or 1 | 0 | 0 |  | 0
1 | 1 | 0 or 1 | 0 | 0 | 0 | 

## Slide 16: Sample 2
1-4 DEMUX
Given an input waveform and two selector switches, can you determine the number of output lines and their respective waveforms?

## Slide 17: Sample 2
Assignment 3
This circuit is of a Full Adder constructed using DEMUX.
Your task is to complete the Truth Table of all inputs and outputs.
Also simulate the input
Show the calculations using the Boolean equations for Sum and Carry out.

## Slide 18: Sample 2
Assignment 3
Attempt these questions from textbook: Digital Fundamentals by Thomas Floyd (11th Edition)
Questions: 1b, 1c, 2a, 2d, 5, 8, 13, 14, 17b, 17d, 17h, 20, 22, 27a, 27c, 30, 31, 33

## Slide 19: THANK YOU
Owais Hussain
+92 345-3174270
owais.hussain@kiet.edu.pk
https://www.researchgate.net/profile/Owais-Hussain-3